## Slide 1: CS143: Disk
Professor Junghoo “John” Cho

## Slide 2: System Architecture
CPU
Main Memory
Disk Controller
...
Disk
Word
(1B – 64B)
~ 100 GB/sec
Block
(512B – 50KB)
~ 10 GB/sec
System Bus

## Slide 3: Magnetic disk vs SSD
Magnetic Disk
  Stores data on a magnetic disk
  Typical capacity: 1TB – 20TB
Solid State Drive (SSD)
  Stores data in NAND flash memory
  Typical capacity: 100GB – 10TB
  Faster than magnetic disk
    Particularly random disk access
  But x5 more expensive and limited write cycles (~2000)

## Slide 6: Structure of a Platter
Track, cylinder, sector (=block, page)
Data is transferred in the unit of “block” (not bytes) to amortize high access delay

## Slide 7: Typical Magnetic Disk
Platter diameter: 2.5-5.25 in
Platters: 1 – 20
Tracks: 1000 – 50,000
Sectors per track: 1000 – 50,000
Sector size: 512 – 50K
Rotation speed: 1000 – 15000 rpm
Overall capacity: 1TB – 20TB

## Slide 8: Access Time
Q: How long does it take to read a page of a disk to memory?
Q: What needs to be done to read a page?
CPU
Memory
page
Disk

## Slide 9: Reading a Page From Disk
Q: What should happen to read the highlighted sector from disk?
Disk arm

## Slide 10: Reading a Page From Disk
Q: What should happen to read the highlighted sector from disk?
Disk arm

## Slide 11: Reading a Page From Disk
Q: What should happen to read the highlighted sector from disk?
Disk arm

## Slide 12: Reading a Page From Disk
Q: What should happen to read the highlighted sector from disk?
Disk arm

## Slide 13: Access Time
Access time = (seek time) + (rotational delay) + (transfer time)

## Slide 14: Seek Time
Time to move a disk head between tracks
Track to track ~ 1ms
Average ~ 10 ms
Full stroke ~ 20 ms
5 - 20x
x
1
N
Cylinders Traveled
Time

## Slide 15: Rotational Delay
Typical disk:
  1000 rpm – 15000 rpm
Q: For 6000 RPM, average rotational delay?
Head Here
Block I Want

## Slide 16: Transfer Time
6000RPM 10,000 sectors/track
Q: How long to read one sector?
Disk Head
Read blocks as
the platter rotates

## Slide 17: Access Time
6000RPM, 10,000 sectors/track
Average access time to read one sector = (seek time) + (rotational delay) + (transfer time)

## Slide 18: Transfer Rate
The rate at which we can transfer data from disk
  Measured in bytes/sec
Q: 6,000 RPM, 10000 sectors/track, 1KB/sector what is the transfer rate?
  Burst transfer rate vs Sustained transfer rate
(Burst) Transfer rate = (RPM / 60) * (sectors/track) * (bytes/sector)

## Slide 19: Random I/O
For magnetic disks:
  Random I/O is VERY expensive compared to sequential I/O
For SSD disks:
  Random I/O is still expensive but not as much as for magnetic disks
Avoid random I/O to minimize delay
 | Magnetic | SSD
Random IO | ~100 IOs/sec | ~100K IOs/sec
Transfer rate | ~ 100MB/sec | ~ 10GB/sec

## Slide 20: Buffers, Buffer pool
Temporary main-memory “cache” for disk blocks
  Avoid future read
  Hide disk latency
  Most DBMS let users change buffer pool size

## Slide 21: Abstraction by OS
Sequential blocks
  No need to worry about head, cylinder, sector
Access to non-adjacent blocks
  Random I/O
Access to adjacent blocks
  Sequential I/O
1
2
3
4
.
.
.
(head, cylinder, sector)

## Slide 22: Things to Remember
Platter, track, cylinder, block (sector)
Access time = seek time + rotational delay + transfer time
Random I/O vs Sequential I/O